## Slide 1: Motherboards

## Slide 2: Motherboard
Main circuit in a computer that connects different parts of a computer together
Analogous to the body's nervous system – allows the CPU to control and communicate with separate parts
Also bridges external components through motherboard ports
Houses CPU, memory and expansion cards

## Slide 3: Main motherboard components
CPU
Chipset
Buses
Memory slots and chips
Expansion slots and cards
Ports and connectors

## Slide 4: Typical motherboard

## Slide 5: Different Types
AT
  Obsolete, patterned after original IBM AT motherboard
Baby AT
  Same design layout as AT, but using smaller area
ATX
  Most common motherboard today
Micro ATX
  Smaller form factor for smaller cases
NLX
  Used in low-profile cases, usually clone PCs
BTX
  BTX form factor designed for better air flow in case; uses ATX power supply

## Slide 6: ATX Motherboard
12” X 9.6”
One-piece power supply connector
Built-in IO ports
Expansion slots parallel to narrow edge of board
Better placement of CPU, RAM, allow better cooling and more expansion slots
Soft-power switching

## Slide 7: ATX Motherboard

## Slide 8: Motherboard components
CPU
  Typically has heat sink or fan attached
  Attached through socket or slot
Motherboard buses
  Network of fine wires on circuit board
  Internal bus
  External bus (expansion bus)

## Slide 9: Motherboard components of note
BIOS Chip
  Stands for Basic Input/Output System
  Allows the hardware in the computer to communicate during startup
  Uses non-volitile memory
PCI Slots
  Used to add extension cards to a machine
  Mainly graphic cards, network cards etc

## Slide 10: Motherboard components of note
CMOS
  Complementary Metal Oxide Semi-conductor
  Little battery used to power CMOS powered memory to hold date time and system setup parameters
  BIOS used to configure CMOS settings
Southbridge
  An integrated circuit responsible for
    Hard drive controller
    I/O controller
    Soundcard
    USB
    BIOS etc
  Although it handles I/O devices, slower I/O devices such as keyboard, non-usb mouse handled by S I/O (Super I/O)

## Slide 11: Motherboard components of note
NorthBridge
  Responsible for communications between RAM and AGP with the CPU.
  Also known as memory controller hub
  Acts as a bridge to the SouthBridge
  Usually closer to the CPU and memory and slightly larger than SouthBridge
With SouthBridge, known as chipset

## Slide 12: Motherboard diagram

## Slide 13: CPU Socket

## Slide 14: Northbridge/Southbridge differences
  Northbridge
    CPU and memory
    High-speed peripherals
    Southbridge
    Onboard video circuitry
  Southbridge
    Peripheral devices
    Non-essential controllers
    Secondary and legacy buses

## Slide 15: Motherboard bus architecture
The Northbridge chips handles IO duties between the CPU and RAM
The Southbridge chip handles IO duties with HDDs, BIOS, USB etc
CPU directly connected to the NorthBridge
NorthBridge acts as a “bridge” to the SouthBridge
Super I/O caters for the slow I/O technologies

## Slide 16: Expansion slots
Used for adding additional circuitry
  Network interfaces
  Video graphics controllers
  Types of expansion slots
    ISA - older
    PCI – short, white
    PCI Express
    AGP – Brown, shorter than PCI

## Slide 17: Expansion slots

## Slide 18: Other motherboard features
Memory slots
Connectors
  Power
  Keyboard
  USB And other peripheral devices

## Slide 19: More on BIOS
Controls essential components
  Keyboard
  Display screen
  Disk drives etc
Three main functions
  Booting the PC
  Verifies hardware
  Provides and interface between hardware and software

## Slide 20: Boot process steps
Power supply initializes
Primary part of BIOS loads to RAM
  CPU access jump address for start of BIOS boot program
Type of boot confirmed
  Cold boot: When PC’s power switched on
  Warm boot: When PC restarted or reset, does not run POST
Power On Self Test (POST) begins
  Error messages given as beep codes
Video adapter software loads

## Slide 21: Boot process steps
Other device BIOS loads
  BIOS startup screen loads
  Error messages displayed as text
CMOS configuration tested
  Test if devices listed in CMOS are present, functioning
Ports assigned and devices configured
Hardware configuration confirmed
  BIOS displays summary screen
Operating system located and loaded
Boot failure:
  When PC unable to complete process and load OS
  Typically caused by loose or missing component