## Slide 1: Anatomy of a computer

## Slide 2: Going to cover
RAM
CPU
  Clock
  Execution
  CPU Cooler
Motherboard
  Components of note
  Bus architecture

## Slide 3: RAM (Random Access Memory)
Data is stored in random locations
Data can be accessed directly regardless of location
In contrast to hard drives etc where they have to spin to the location of the data before being able to access it.
Essentially a set of memory chips soldered onto a stick of circuit board

## Slide 4: RAM
Blazing fast when compared to hard drives
RAM storage is volatile
  Lost once computer is turned off
  Like short term memory
Very important in software programs
  Keep low memory footprint
  OutOfMemoryException (beware)

## Slide 5: CPU (Central Processing Unit)
Also known as the processor/microprocessor
Known as the “brains” of the computer
Housed in a single chip
Inserted directly into a CPU socket, pin side down on the motherboard
Modern CPUs are attached to a heat sink to dissipate heat

## Slide 6: CPU (Central Processing Unit)
Anonymous processing
Uses a clock
Executes instructions
Uses a bus
Can have many cores

## Slide 7: CPU Clock
Used to “sync” instructions in a computer
Typical clock signal, square signal changing from 0 to 1 at a fixed rate
3 full cycles shown (ticks)
Measured in Hertz, 100MHz = 100 million ticks per second

## Slide 8: CPU Clock
Clock cycle for each instruction is stored in tables
Queues instructions based on “delay”
Two identical processors, better clock speed = better performance
CPUs have many execution units
Also has an external clock for transferring data to and from RAM

## Slide 9: CPU External clock
Used when transferring data to and from RAM
When internal clock speeds got too fast, a slower external clock was needed

## Slide 10: Block diagram of a CPU
Dotted line represents the CPU body
RAM outside CPU
Red arrow (external clock)
Other arrows (Internal clock)

## Slide 11: Memory cache
High performance memory
Can work at same speed as the CPU clock
Static memory, consumes more power than dynamic memory but is much faster
Cache controller manages memory cache
Bigger the memory cache, less likely direct memory access is required
Hit = data in memory cache, Miss = data in RAM

## Slide 12: Instruction/Data Cache
L1 Instruction cache works as an input cache, lining up instructions to be executed
Data cache simply an output cache
L1 Instruction cache particularly efficient for “looping behaviour” as required instructions are closer to the fetch unit

## Slide 13: Fetch/Decode/Execute
Also known as an instruction cycle or FDX
Fetch
  Gets data from RAM via an address bus and stores internally in CPU. Data received by CPU via data bus
Decode
  CPU decodes the instruction just fetched and prepares various areas of chip for next step
Execute
  Instruction is carried out on the data and output stored in data cache

## Slide 14: CPU Cooler
Also known as a heat sink or CPU fan
Often bundled with CPUs
Other heat sinks are used in a computer
Transfers thermal energy from a higher temperature device to a lower temperature fluid medium

## Slide 15: Motherboard
Main circuit in a computer that connects different parts of a computer together
Analogous to the body's nervous system – allows the CPU to control and communicate with separate parts
Also bridges external components through motherboard ports
Houses CPU, memory and expansion cards

## Slide 16: Motherboard diagram

## Slide 17: Motherboard components of note
BIOS Chip
  Stands for Basic Input/Output System
  Allows the hardware in the computer to communicate during startup
  Uses non-volitile memory
PCI Slots
  Used to add extension cards to a machine
  Mainly graphic cards, network cards etc

## Slide 18: Motherboard components of note
CMOS
  Complementary Metal Oxide Semi-conductor
  Little battery used to power CMOS powered memory to hold date time and system setup parameters
Southbridge
  An integrated circuit responsible for
    Hard drive controller
    I/O controller
    Soundcard
    USB
    BIOS etc
  Although it handles I/O devices, slower I/O devices such as keyboard, non-usb mouse handled by S I/O (Super I/O)

## Slide 19: Motherboard components of note
NorthBridge
  Responsible for communications between RAM and AGP with the CPU.
  Also known as memory controller hub
  Acts as a bridge to the SouthBridge
  Usually closer to the CPU and memory and slightly larger than SouthBridge

## Slide 20: Motherboard bus architecture
The Northbridge chips handles IO duties between the CPU and RAM
The Southbridge chip handles IO duties with HDDs, BIOS, USB etc
CPU directly connected to the NorthBridge
NorthBridge acts as a “bridge” to the SouthBridge
Super I/O caters for the slow I/O technologies

## Slide 21: What happens when you start a program?
Data transferred from hard disk to RAM
  Program is a set of instructions for a CPU
CPU loads the program from RAM to in-memory CPU
The data (instructions) now inside the CPU gets executed (fetch-decode-execute)
What happens next depends on the program
  Display on screen
  Continue to load from RAM