## Slide 1: Mobile app concepts
Mobile cellular network fundamentals and different generations

## Slide 2: Cellular Network Basics
There are many types of cellular services; before delving into details, focus on basics (helps navigate the “acronym soup”)
Cellular network/telephony is a radio-based technology; radio waves are electromagnetic waves that antennas propagate
Most signals are in the 850 MHz, 900 MHz, 1800 MHz, and 1900 MHz frequency bands
Cell phones operate in this frequency range (note the logarithmic scale)

## Slide 3: Cellular Network
Base stations transmit to and receive from mobiles at the assigned spectrum
  Multiple base stations use the same spectrum (spectral reuse)
The service area of each base station is called a cell
Each mobile terminal is typically served by the ‘closest’ base stations
  Handoff when terminals move

## Slide 4: Cellular Network Generations
It is useful to think of cellular Network/telephony in terms of generations:
  0G: Briefcase-size mobile radio telephones
  1G: Analog cellular telephony
  2G: Digital cellular telephony
  3G: High-speed digital cellular telephony (including video telephony)
  4G: IP-based “anytime, anywhere” voice, data, and multimedia telephony at faster data rates than 3G (to be deployed in 2012–2015)

## Slide 5: Evolution of Cellular Networks
1G
2G
3G
4G
2.5G

## Slide 6: The Multiple Access Problem
The base stations need to serve many mobile terminals at the same time (both downlink and uplink)
All mobiles in the cell need to transmit to the base station
Interference among different senders and receivers
So we need multiple access scheme

## Slide 7: Multiple Access Schemes
Frequency Division Multiple Access (FDMA)
Time Division Multiple Access (TDMA)
Code Division Multiple Access (CDMA)
3 orthogonal Schemes:

## Slide 8: Frequency Division Multiple Access
Each mobile is assigned a separate frequency channel for the duration of the call
Sufficient guard band is required to prevent adjacent channel interference
Usually, mobile terminals will have one downlink frequency band and one uplink frequency band
Different cellular network protocols use different frequencies
Frequency is a precious and scare resource. We are running out of it!
frequency

## Slide 9: Time Division Multiple Access
Time is divided into slots and only one mobile terminal transmits during each slot
  Like during the lecture, only one can talk, but others may take the floor in turn
Each user is given a specific slot. No competition in cellular network
  Unlike Carrier Sensing Multiple Access (CSMA) in WiFi
Guard time – signal transmitted by mobile terminals at different locations do no arrive at the base station at the same time

## Slide 10: Code Division Multiple Access
Use of orthogonal codes to separate different transmissions
Each symbol of bit is transmitted as a larger number of bits using the user specific code – Spreading
  Bandwidth occupied by the signal is much larger than the information transmission rate
  But all users use the same frequency band together
Orthogonal among users

## Slide 11: 2G(GSM)

## Slide 12: GSM
Abbreviation for Global System for Mobile Communications
Concurrent development in USA and Europe in the 1980’s
The European system was called GSM and deployed in the early 1990’s

## Slide 13: GSM Services
    Voice, 3.1 kHz
Short Message Service (SMS)
  1985 GSM standard that allows messages of at most 160 chars. (incl. spaces) to be sent between handsets and other stations
  Over 2.4 billion people use it; multi-billion $ industry
General Packet Radio Service (GPRS)
  GSM upgrade that provides IP-based packet data transmission up to 114 kbps
  Users can “simultaneously” make calls and send data
  GPRS provides “always on” Internet access and the Multimedia Messaging Service (MMS) whereby users can send rich text, audio, video messages to each other
  Performance degrades as number of users increase
  GPRS is an example of 2.5G telephony – 2G service similar to 3G

## Slide 14: GSM Channels
Physical Channel: Each timeslot on a carrier is referred to as a physical channel
Logical Channel: Variety of information is transmitted between the MS and BTS. Different types of logical channels:
  Traffic channel
  Control Channel
Downlink
Uplink
Channels

## Slide 15: GSM Frequencies
Originally designed on 900MHz range, now also available on 800MHz, 1800MHz and 1900 MHz ranges.
Separate Uplink and Downlink frequencies
  One example channel on the 1800 MHz frequency band, where RF carriers are space every 200 MHz
1710 MHz
1880 MHz
1805 MHz
1785 MHz
UPLINK FREQUENCIES
DOWNLINK FREQUENCIES
UPLINK AND DOWNLINK FREQUENCY SEPARATED BY 95MHZ

## Slide 16: GSM Architecture

## Slide 17: Mobile Station (MS)
MS is the user’s handset and has two parts
Mobile Equipment
  Radio equipment
  User interface
  Processing capability and memory required for various tasks
    Call signalling
    Encryption
    SMS
  Equipment IMEI number
Subscriber Identity Module

## Slide 18: Subscriber Identity Module
A small smart card
Encryption codes needed to identify the subscriber
Subscriber IMSI number
Subscriber’s own information (telephone directory)
Third party applications (banking etc.)
Can also be used in other systems besides GSM, e.g., some WLAN access points accept SIM based user authentication

## Slide 19: Location Updates
The cells overlap and usually a mobile station can ‘see’ several transceivers (BTSes)
The MS monitors the identifier for the BSC controlling the cells
When the mobile station reaches a new BSC’s area, it requests an location update
The update is forwarded to the MSC, entered into the VLR, the old BSC is notified and an acknowledgement is passed back

## Slide 20: 3G, 3.5G and 4G (LTE)

## Slide 21: 3G Overview
3G is created by ITU-T and is called IMT-2000

## Slide 22: Evolution from 2G
IS-95
IS-136 & PDC
GSM-
EDGE
GPRS
HSCSD
IS-95B
Cdma2000-1xRTT
Cdma2000-1xEV,DV,DO
Cdma2000-3xRTT
W-CDMA
EDGE
TD-SCDMA
2G
3G
2.5G
3GPP
3GPP2

## Slide 23: Service Roadmap
Improved performance, decreasing cost of delivery
Typical average bit rates (peak rates higher)
WEB browsing
Corporate data access
Streaming audio/video
Voice & SMS
Presence/location
xHTML browsing
Application downloading
E-mail
MMS picture / video
Multitasking
3G-specific services take advantage of higher bandwidth and/or real-time QoS
A number of mobile services are bearer independent in nature
HSDPA
1-10
Mbps
WCDMA
2
Mbps
EGPRS
473
kbps
GPRS
171
kbps
GSM
9.6
kbps
Push-to-talk
Broadband
in wide area
Video sharing
Video telephony
Real-time IP
multimedia and games
Multicasting
CDMA 2000-EVDO
CDMA 2000-EVDV
CDMA 2000 1x

## Slide 24: GSM Evolution to 3G
GSM
9.6kbps (one timeslot)
GSM Data
Also called CSD
GSM
General Packet Radio Services
Data rates up to ~ 115 kbps
Max: 8 timeslots used as any one time
Packet switched; resources not tied up all the time
Contention based. Efficient, but variable delays
GSM / GPRS core network re-used by WCDMA (3G)
GPRS
HSCSD
High Speed Circuit Switched Data
Dedicate up to 4 timeslots for data connection ~ 50 kbps
Good for real-time applications c.w. GPRS
Inefficient -> ties up resources, even when nothing sent
Not as popular as GPRS (many skipping HSCSD)
EDGE
Enhanced Data Rates for Global Evolution
Uses 8PSK modulation
3x improvement in data rate on short distances
Can fall back to GMSK for greater distances
Combine with GPRS (EGPRS) ~ 384 kbps
Can also be combined with HSCSD
WCDMA

## Slide 25: UMTS
Universal Mobile Telecommunications System (UMTS)
UMTS is an upgrade from GSM via GPRS or EDGE
The standardization work for UMTS is carried out by Third Generation Partnership Project (3GPP)
Data rates of UMTS are:
  144 kbps for rural
  384 kbps for urban outdoor
  2048 kbps for indoor and low range outdoor
Virtual Home Environment (VHE)

## Slide 26: 3.5G (HSPA)
High Speed Packet Access (HSPA) is an amalgamation of two mobile telephony protocols, High Speed Downlink Packet Access (HSDPA) and High Speed Uplink Packet Access (HSUPA), that extends and improves the performance of existing WCDMA protocols
3.5G introduces many new features that will enhance the UMTS technology in future. 1xEV-DV already supports most of the features that will be provided in 3.5G. These include:
- Adaptive Modulation and Coding
- Fast Scheduling
- Backward compatibility with 3G
- Enhanced Air Interface

## Slide 27: 4G (LTE)
LTE stands for Long Term Evolution
Next Generation mobile broadband technology
Promises data transfer rates of 100 Mbps
Based on UMTS 3G technology
Optimized for All-IP traffic

## Slide 28: Advantages of LTE

## Slide 29: Comparison of LTE Speed