## Slide 1: Hard Drive

## Slide 2: Definition
A hard disk drive (HDD) is a data storage device used for storing and retrieving digital information using rapidly rotating disks (platters) coated with magnetic material.
A HDD retains its data even when powered off.
Data is read in a random-access manner, meaning individual blocks of data can be stored or retrieved in any order rather than sequentially.

## Slide 3: HDD Internals

## Slide 4: Main components
Platters
  Mounted and rotated on spindle in sealed enclosure
  Has a thin film of ferro-magnetic material
  Binary bits determined by change in direction of magnetisation
Spindle
  Responsible for spinning the disks at a fast pace
  Today on average sins between 5,400 to 7200 rpm
Actuator
  Motor that positions read/write head assembly across the spinning platters

## Slide 5: Main components
Actuator arm
  Position controlled by the actuator, by being mounted on the actuator axis, supports read/write heads
Magnetic read/write heads
  Used to detect and modify the magnetization of the material immediately under it
Actuator axis
  Controls the angled position of the actuator arms via the actuator
Jumper pins
  Used in ATA HDDs to configure master/slave
2 motors involved
  Spindle
  Actuator

## Slide 6: Drive geometry

## Slide 7: Drive geometry
Heads
  1 read/write head per platter
Tracks
  Data written in concentric rings (16000+)
Cylinder
  Collection of tracks at same actuator arm position on all platters
Sector
  Smallest accessible portion of data on track
  512 bytes, up to 63 per track

## Slide 8: Zoned Bit Recording
Improves capacity
In example shown:
  20 tracks
  5 zones
  Blue = 5*16 sectors
  Cyan = 5*14 sectors
  Red 3*9 sectors
Don’t want to limit outer to 9 sectors

## Slide 9: HDD Characteristics
Capacity
  Determined by the geometry of the drive
  E.g 512bytes/sector*60 sectors/track *cylinders * heads etc.
  Currently measured in GB (Ranges from 250 – 1TB)
Spin speed
  Modern day drives usually 5,400 to 7,200 rpm
  Performance differs based on speed
  Some servers can have up to 15,000 rpm

## Slide 10: HDD Characteristics
Seek time
  Measures the time it takes the head assembly on the actuator arm to travel to the track of the disk where the data will be read or written
  Typically about 9ms
Rotational latency
  Time for sector to travel to head after head in place
  Measured in milliseconds
  Usually seek time takes longer
  Faster spin speed, faster rotational latency

## Slide 11: HDD Characteristics
Average rotational latency
  Time it takes disc to turn 180 degrees
  Worst case is having to go a full revolution
Access time
  Full amount of time to move head and access sector
  Access time = (Seek time + Rotational Latency)

## Slide 12: HDD Characteristics
Interface
  Technology for connecting HDD (ATA, SATA etc)
  Determine the rate of data transfer
Disk cache size
  Typically 16-32 MB
  Stores frequently accessed data
  Minimises the number of physical seeks
Data transfer rate
  Amount of data transferred in 1 second
  External (RAM to disk cache)
  Internal (Disk cache to platter)

## Slide 13: PATA vs SATA
PATA
  Also called ATA and IDE developed in 1980s
  Modern motherboards don’t have PATA connectors
  Slower (Max of 133 Gbps)
  Connectors are flat ribbon cables of 40-80 wires
SATA
  Introduced in 2003
  Faster (up to 600 Gbps)
  Spins at higher RPMs
  Connectors are much smaller and thinner cables

## Slide 14: PATA Drive Master/Slave
Two PATA drives can share ribbon cable and controller, and can be configured using jumpers as master/slave

## Slide 15: Preparing a drive for use
Must be “high-level” formatted
  E.g. FAT32, NTFS
  Low level formatting done by manufacturer
  Prepares drive for managing files
Must be partitioned
  Divided into sections with different drive letters
  1 HDD can have as many as 4 partitions
  Active partition = partition used to start the PC
  System partition
    Contains hardware files used by the OS
    Usually = system partition

## Slide 16: Managing hard drives
Back ups
Error checking (CHECKDISK)
Disk defragmentation (DISK DEFRAG UTILITY)
Fault tolerance
Troubleshooting
  Faulty adapter
  Faulty disk (defect, virus etc)
  Adapter and disk not connected correctly